## Slide 1
Q1 2025: 17/12/2024 – 31/03/2025
Core IDCC(c) Operational KPI report
External // run KPI report

## Slide 2: External // run KPI report
Introduction, reporting period and limitations
Context
  According to Article 26(4) of the Core FB ID CCM, “Core TSOs shall continuously monitor the effects and the performance of the application of this methodology during the parallel run. And shall develop, in coordination with the Core regulatory authorities, the Agency and stakeholders, the monitoring and performance criteria and report on the outcome of this monitoring on quarterly basis in a report”.
  IDCC(c) external // run started on 17th of December 2024. The results of IDCC(c) have been published on [JAO website]
Reporting period
  This report covers 3.5 months (17/12/2024 – 31/03/2025) of IDCC(c) EXT //run results in the Core region.
  11 business days have been excluded from the computation of KPIs due to:
  For 4 business days the IDCC(c) process failed due to the merging package delivery. The implementation of an automatic merging solution is deployed since 13th February, and this issue is solved. For the rest of the excluded days, the problems identified were occasional and solved.
  For information, the business days with an IDCF of 1:15 instead of 2:15:
    29/12/2024, 30/12/2024, 09/01/2025, 17/01/2025, 23/01/2025, 24/01/2025, 30/03/2025
Disclaimers (if any)
  Until 07/03 the results are impacted by incorrect AACs due to incorrect MTU configuration for some border directions.
  TSOs are still developing their individual validation tools. ĆEPS, Elia, RTE, SEPS perform validation (Status on 02/04)
BD | Reason | Fallback/ Process failure
18/12/2024 | Manual selection of CGM of the incorrect BD | DA Domain AAC Fallback
26/12/2024 | Isolated issue with duplicated merging request | 
28/12/2024 | Merging package delivery failed | 
23/01/2025 | 15 min MTU go-live FR borders – rejected AACs | Process failure
04/02/2025 | Merging package delivery failed | DA Domain AAC Fallback
07/03/2025 | Viking link configuration missing in new tool version | 
BD | Reason | Fallback/ Process failure
14/03/2025 | XBID integration testing – rejected merging package but delivered timely | DA Domain AAC Fallback
19/03/2025 | AAC incorrect time resolution | N/A
22/03/2025 | Failure to receive AAC timely | Process failure
28/03/2025 | Excluded for the KPIs 2A, 3A and 4A because IDCC(b) process failure – No comparison possible | 
30/03/2025 | Hour change - Clock change issue | N/A

## Slide 3: External // run KPI report
Overview of the KPIs covered during the // run
ATC related KPIs
    Duration curve of Number of Core Oriented Bidding Zone Borders with Zero or Negative ID ATCs​
    Frequency of Zero and Negative ID ATCs by Oriented Core Bidding Zone Border​
      Delta comparison with IDCC(b) run at ~4:30
    Frequency of isolated Core Bidding Zones of zero (or negative) ID ATCs in import, export and both directions​
      Delta comparison with IDCC(b) run at ~4:30
    Mean positive ID ATCs by Oriented Core Bidding Zone Border
      Delta comparison with IDCC(b) run at ~4:30
    TSOs’ adjustment after validation
    Share of MTUs with intervention during IVA validation per TSO (IVA aggregations per TSO)
    Limiting elements
    Limiting constraints of the ATC domain​
      20 most limiting ATC constraints
      Mean and Max of ATC limiting constraints
      Mean and Max of ATC limiting constraints per TSO
      ATC Based Validation - Aggregations
    Most often used pre-solved CNECs​
      20 most limiting pre-solved constraints
      Mean and Max of pre-solved constraints
      Mean and Max of pre-solved constraints per TSO
    Net positions
    Min and Max Net Positions per Bidding Zone​
      Based on final FB domain
      Based on final ID ATC
    Reading Guide with a detail description of the KPIs available on [JAO]
Included only as of IDCC(c) go-live date

## Slide 4: External // run KPI report
Conclusions
  Core TSOs are glad to report the current process stability with ~92% of business days successfully completed.
  According to the ATC related KPIs (ATCs, bidding zone isolation), which compare the available cross-zonal capacities at ~4:30 with and without IDCC(c) run, there is an overall "reflow" effect of the IDCC(c) calculation, in which the available capacity domain space is redistributed across all borders.
  This results in a lower negative or zero ATC frequency, which leads to less bidding zone isolation frequency. A general decrease of negative ATCs and of bidding zone isolation, means reopening border directions in the IDCC(c) calculation, which were closed during IDCC(b) for longer periods. This decreases the ID ATC levels on other borders (those who would be used if the considered borders were not reopened). Instead of less often open border directions, these are more often open with in general a bit less positive ID ATCs everywhere else.
  In short the available capacities are redistributed around the market point, or "reflowed" as we call it.
  This effect has been quite stable since the start of the parallel run and was expected by experts. It is thus concluded that the parallel run is going according to expectations.
  Disclaimer: not all TSO's have started performing the individual validation step. This will be resolved soon Core TSOs deem the current // run results representative, thus no significant impact is expected from the deployment of individual validation

## Slide 5: KPI 2
Frequency of Zero and Negative ID ATCs by Oriented Core Bidding Zone Border​

## Slide 6: KPI 2A - Delta comparison with IDCC(b) run at ~4:30
Frequency of Zero and Negative ID ATCs by Oriented Core Bidding Zone Border​

## Slide 7: KPI 3
Frequency of isolated Core Bidding Zones of zero (or negative) ID ATCs in import, export and both directions ​​

## Slide 8: KPI 3A - Delta comparison with IDCC(b) run at ~4:30
Frequency of isolated Core Bidding Zones of zero (or negative) ID ATCs in import, export and both directions ​​

## Slide 9: KPI 4
Mean positive ID ATCs by Oriented Core Bidding Zone Border

## Slide 10: KPI 4A - Delta comparison with IDCC(b) run at ~4:30
Mean positive ID ATCs by Oriented Core Bidding Zone Border

## Slide 11: KPI 4A - Delta comparison with IDCC(b) run at ~4:30
Mean positive ID ATCs by Oriented Core Bidding Zone Border

## Slide 12: KPI 5
Share of MTUs with intervention during IVA validation per TSO (IVA aggregations per TSO)

## Slide 13: KPI 6A & 6B - Limiting constraints of the ATC domain​
20 most limiting ATC constraints & Mean and Max of ATC limiting constraints

## Slide 14: KPI 6A & 6B - Limiting constraints of the ATC domain​
20 most limiting ATC constraints & Mean and Max of ATC limiting constraints

## Slide 15: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO - APG

## Slide 16: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO - Elia

## Slide 17: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – CEPS

## Slide 18: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – Tennet Germany

## Slide 19: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – Transnet

## Slide 20: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – Amprion

## Slide 21: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – 50Hertz

## Slide 22: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – RTE

## Slide 23: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – HOPS

## Slide 24: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – MAVIR

## Slide 25: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – Tennet Netherlands

## Slide 26: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – PSE

## Slide 27: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – Transelectrica

## Slide 28: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO – ELES

## Slide 29: KPI 6C - Limiting constraints of the ATC domain​
Mean and Max of ATC limiting constraints per TSO - SEPS

## Slide 30: KPI 6D
ATC Based Validation - Aggregations
No ATC validation performed since start of the IDCC(c) ext//run

## Slide 31: KPI 7A & 7B - Most often used pre-solved CNEsC​
20 most limiting pre-solved constraints & Mean and Max of pre-solved constraints

## Slide 32: KPI 7A & 7B - Most often used pre-solved CNECs​
20 most limiting pre-solved constraints & Mean and Max of pre-solved constraints

## Slide 33: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO - APG

## Slide 34: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO - Elia

## Slide 35: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO – CEPS

## Slide 36: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO – Tennet Germany

## Slide 37: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO - Transnet

## Slide 38: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO - Amprion

## Slide 39: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO – 50Hertz

## Slide 40: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO – RTE

## Slide 41: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO – HOPS

## Slide 42: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO – MAVIR

## Slide 43: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO – Tennet Netherlands

## Slide 44: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO – PSE

## Slide 45: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO – Transeletrica

## Slide 46: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO – ELES

## Slide 47: KPI 7C - Most often used pre-solved CNECs​ ​
Mean and Max of pre-solved constraints per TSO - SEPS

## Slide 48: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – Austria

## Slide 49: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – Belgium

## Slide 50: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – Czech Republic

## Slide 51: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – Germany

## Slide 52: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – Croatia

## Slide 53: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – France

## Slide 54: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – Hungary

## Slide 55: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – Netherlands

## Slide 56: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – Poland

## Slide 57: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – Romania

## Slide 58: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – Slovenia

## Slide 59: KPI 8A – Min and Max Net Positions per Bidding Zone​
Based on final FB domain – Slovakia

## Slide 60: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – Austria

## Slide 61: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – Belgium

## Slide 62: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – Czech Republic

## Slide 63: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – Germany

## Slide 64: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – France

## Slide 65: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – Croatia

## Slide 66: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – Hungary

## Slide 67: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – Netherlands

## Slide 68: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – Poland

## Slide 69: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – Romania

## Slide 70: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – Slovenia

## Slide 71: KPI 8B – Min and Max Net Positions per Bidding Zone​
Based on final ID ATC – Slovakia